## Slide 1
SK0-005
COMPTIA SERVER+
COURSE SLIDES · WSQ
CompTIA Certified Server+ Training
WSQ Course Code: TGS-2024048318
Conducted by Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Version v4.0 · 19 August 2026
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved. · www.tertiarycourses.com.sg

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
1

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
• It is mandatory to take the AM, PM and Assessment digital attendance for WSQ-funded courses.
• The trainer/administrator displays the digital attendance QR code from the SSG portal.
• Scan the QR code with your mobile phone camera and submit your attendance.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 4
YOUR TRAINER · GENERAL
About the Trainer
?
Your Trainer
General Trainer template — to be completed by the trainer
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 5
YOUR TRAINER
About the Trainer
AA
Dr Alfred Ang
Principal Trainer Tertiary Infotech Academy Pte Ltd
ROLE
Principal Trainer, Tertiary Infotech Academy Pte Ltd
CERTIFICATION
CompTIA Server+ / infrastructure certified — server hardware, storage, virtualization and data-centre operations.
DELIVERS
WSQ courses on server administration, cloud infrastructure, networking and cybersecurity.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name and organisation / role.
• Your experience with servers, storage, networking or Linux/Windows administration (if any).
• What you want to be able to build, secure or troubleshoot after this course.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is too small.
3
Mutual respect: agree to disagree.
4
One conversation at a time.
5
Be punctual; return from breaks on time.
6
75% attendance is required.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 8
COURSE PORTAL · LMS-TMS
Download Your Course Material
🔒 lms-tms.tertiaryinfotech.com
My Courses › CompTIA Server+
Trainer Slides (PPT)
⬇ Download
Learner Slides (PDF)
⬇ Download
Learner Guide (PDF)
⬇ Download
Lesson Plan (PDF)
⬇ Download
1
Log in
Go to lms-tms.tertiaryinfotech.com and sign in with your enrolment email.
2
Open the course
Select CompTIA Certified Server+ Training from My Courses.
3
Download
Download the Trainer Slides, Learner Slides, Learner Guide and Lesson Plan.
4
Use in the open book
Keep the slides and Learner Guide open during the assessment.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 9
SCHEDULE
Lesson Plan — 3 Days, 8 hours/day
Days 1–2
Day 3 & timing
• Day 1 — Server Hardware, Storage & OS Administration
– Topic 1: Server Hardware Installation & Management (Labs 1–5)
– Topic 2: Server Administration begins (Labs 6–13)
• Day 2 — Networking, Virtualization, Security & Disaster Recovery
– Topic 2: Server Administration (Labs 14–17)
– Topic 3: Security & Disaster Recovery (Labs 18–27)
• Day 3 — Troubleshooting & Final Assessment
– Topic 4: Troubleshooting (Labs 28–33)
– Revision and exam preparation
– Final Assessment (WA + PP)
• Daily timing
– 9:00am–6:00pm · 1-hour lunch · tea breaks within
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
8

## Slide 10
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
Hardware & Storage
Rack, cable, power and cool servers; deploy RAID and shared storage; manage firmware and out-of-band.
2
Server Administration
Install operating systems and file systems; configure IP/DNS/DHCP/VLANs; run roles, HA, virtualization and scripts.
3
Security & DR
Encrypt data, harden hosts, manage identity and access, decommission media, and plan backups and disaster recovery.
4
Troubleshooting
Diagnose hardware, storage, OS, software and network faults with a structured methodology.
5
Exam readiness
Map every hands-on skill to the CompTIA Server+ SK0-005 exam domains and pass the exam.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 11
Briefing for Assessment
• Place phones and other materials under the table or on the floor.
• No photos or recording of assessment scripts.
• No discussion during the assessment.
• Use a black/blue pen for hard-copy assessments.
• No liquid paper / correction tape.
• Scripts are collected when time is up.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 12
FINAL ASSESSMENT
Assessment
• Written Assessment (WA) — Short-Answer Questions (SAQ), 1 hour, open book.
• Practical Performance (PP) — hands-on server administration tasks on the Killercoda Ubuntu playground, 1 hour, open book.
• Format: Open Book — slides, Learner Guide and approved materials only.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
• An appeal process is available if required.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 13
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit WA (SAQ) then PP — open book
▶
4
Submit your answers on the LMS
▶
5
Sign the Assessment Summary Record
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 14
CORE CONCEPTS
Server Fundamentals
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 15
OVERVIEW
What is a Server?
1
Purpose-built
Hardware and an OS built to provide services — web, file, database, directory — reliably to many clients.
2
Availability first
Redundant power, storage and networking so the service stays up; measured against SLAs, RPO and RTO.
3
Managed remotely
Out-of-band controllers (IPMI/iDRAC/iLO) run the server even when the OS is down.
4
The SK0-005 role
Install, configure, secure and troubleshoot servers on-premises and in the cloud.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 16
WHAT YOU'LL MASTER
The Four Server+ Exam Domains
Install & administer
• Hardware, racking, power
• Storage & RAID, OS install
• Networking, roles, HA, scripting
Secure & recover
• Data & physical security
• IAM, hardening, decommissioning
• Backup & disaster recovery
Troubleshoot
• Structured 6-step method
• Hardware, storage, OS faults
• Network faults & DR validation
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 17
WHY IT MATTERS
Install, administer, secure, troubleshoot.
The four SK0-005 domains follow the real life of a server — from racking and OS install to hardening, backup and fault diagnosis.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 18
DEPLOYMENT MODELS
On-premises vs. cloud
Your data centre
Public / private / hybrid
• On-premises
– You own the hardware and data centre
– Full control of security and latency
– Capital cost, capacity planning, maintenance
• Cloud (IaaS/PaaS/SaaS)
– Rented infrastructure, pay-as-you-go
– Elastic scaling and managed services
– Shared-responsibility security model
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 19
YOUR WORKBENCH
Your Lab Environment — Killercoda
• Every hands-on lab runs on the free Killercoda Ubuntu playground — a disposable Linux VM in the browser.
• Portal: https://killercoda.com/playgrounds/scenario/ubuntu — no local install or physical hardware needed.
• Install any tool with apt inside the throw-away VM; reset the playground between state-changing labs.
• Hardware-only concepts use software equivalents: loopback disks for RAID, ip link for NICs, KVM for VMs, dmidecode/ipmitool for hardware inspection.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 20
ALL FREE · KILLERCODA + APT
Free Tools You'll Use
1
Hardware & storage
dmidecode, lshw, ipmitool, mdadm, lvm2, parted, smartctl — inspect, build and monitor server hardware and disks.
2
Networking
ip, bind9, isc-dhcp-server, ufw/nftables, tcpdump, dig, mtr — configure and diagnose server networking.
3
Roles & virtualization
nginx, samba, mariadb, slapd, qemu-kvm/libvirt, haproxy/keepalived — stand up services and high availability.
4
Security
cryptsetup, openssl, sudo/PAM, auditd, lynis, unattended-upgrades, shred/nwipe — encrypt, harden and sanitize.
5
Backup & DR
tar, rsync, restic, lsyncd — full/incremental backups, replication and site failover.
6
Online helpers
IP Calculator (alfredang.github.io/ipcalculator), the Cybersecurity Simulator, and the Pcap/Regex tools.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 21
TOPIC 01
Server Hardware Installation and Management
Racking & power · storage & RAID · out-of-band management & firmware
01
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 22
EXAM WEIGHTING 18%
Key Concepts — Server Hardware Installation and Management
1
Form factors & racking
Rack (1U/2U/4U) vs. tower vs. blade; rack units, rail kits, cable management, weight distribution and airflow direction (front-to-back).
2
Power & cooling
Redundant PSUs, dual power feeds, PDUs and UPS; hot vs. cold aisle containment; environmental targets for temperature and humidity.
3
RAID levels
RAID 0/1/5/6/10 and JBOD — capacity and fault-tolerance formulas; hardware vs. software RAID; when RAID 6 or RAID 10 wins.
4
Shared storage
DAS vs. NAS vs. SAN; NFS/SMB (file) vs. iSCSI/Fibre Channel (block); LUNs, and capacity planning with growth headroom.
5
Out-of-band management
IPMI/BMC, iDRAC/iLO for lights-out control; firmware/BIOS/UEFI updates and the update order.
6
Hot-swap & maintenance
Hot-swappable drives, PSUs and fans; hot-add vs. cold maintenance; component replacement without downtime.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 23
WHAT YOU'LL DO
Hands-On Labs — Server Hardware Installation and Management
Labs 1–2
• Server Form Factors, Racking, and Power Planning
• Storage Deployment: RAID 0/1/5/6/10 with mdadm
Labs 3–4
• LVM Provisioning and Capacity Planning
• Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
Labs 5–5
• Out-of-Band Management, BIOS/UEFI, and Firmware
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 24
TOPIC 01 · HANDS-ON
Server Form Factors, Racking, and Power Planning
LAB 1
The learner inventories a running system with dmidecode/lshw and plans a 42U rack layout with power and cooling rules the way a data-centre technician would.
You'll build
A rack layout plan plus a hardware inventory and power-budget sanity check.
Tools: dmidecode, lshw, lscpu, lspci, lsusb
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 25
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
1
STEP 1 OF 8
Install the hardware inventory tools
$ apt update && apt install -y dmidecode lshw pciutils usbutils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 26
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
2
STEP 2 OF 8
Identify the running system as a rack-mount server
$ dmidecode -t system | grep -E "Manufacturer|Product|Serial"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 27
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
3
STEP 3 OF 8
Read chassis type and U-height
$ dmidecode -t chassis | grep -E "Type|Height|Power"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 28
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
4
STEP 4 OF 8
Inventory CPU, RAM, bus types and expansion cards
$ lscpu | head -20
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 29
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
5
STEP 5 OF 8
List PCI/PCIe buses and cards
$ lspci | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 30
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
6
STEP 6 OF 8
Get the model string for a hardware compatibility list (HCL) check
$ dmidecode -s system-product-name
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 31
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
7
STEP 7 OF 8
Plan a 42U rack layout: heaviest at bottom, redundant power on separate circuits
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 32
LAB 1 · Server Form Factors, Racking, and
Server Form Factors, Racking, and Power Planning
8
STEP 8 OF 8
Do a power-budget sanity check against the PDU and breaker (80% rule)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 33
LAB 1 · VERIFY
Server Form Factors, Racking, and Power Planning
✅ Test it
The learner verifies success by reading chassis/CPU/memory data and producing a rack layout that respects U sizing, weight balancing, cooling and redundant power.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 34
TOPIC 01 · HANDS-ON
Storage Deployment: RAID 0/1/5/6/10 with mdadm
LAB 2
The learner builds every RAID level the exam tests on loopback files with mdadm, then fails and rebuilds an array to observe resync.
You'll build
Working RAID 0/1/5/6/10 and JBOD arrays plus a completed rebuild.
Tools: mdadm, losetup, mkfs.ext4
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 35
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
1
STEP 1 OF 9
Install mdadm
$ apt update && apt install -y mdadm
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 36
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
2
STEP 2 OF 9
Create six loopback disks that behave like drives
$ for i in 1 2 3 4 5 6; do truncate -s 200M disk$i.img; losetup /dev/loop$i disk$i.img; done
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 37
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
3
STEP 3 OF 9
Build a RAID 0 stripe (N x disk, no redundancy)
$ mdadm --create /dev/md0 --level=0 --raid-devices=2 /dev/loop1 /dev/loop2
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 38
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
4
STEP 4 OF 9
Build a RAID 1 mirror (survives 1 disk failure)
$ mdadm --create /dev/md1 --level=1 --raid-devices=2 /dev/loop1 /dev/loop2
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 39
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
5
STEP 5 OF 9
Build a RAID 5 single-parity array
$ mdadm --create /dev/md5 --level=5 --raid-devices=3 /dev/loop1 /dev/loop2 /dev/loop3
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 40
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
6
STEP 6 OF 9
Build a RAID 6 double-parity array
$ mdadm --create /dev/md6 --level=6 --raid-devices=4 /dev/loop1 /dev/loop2 /dev/loop3 /dev/loop4
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 41
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
7
STEP 7 OF 9
Build a RAID 10 stripe of mirrors
$ mdadm --create /dev/md10 --level=10 --raid-devices=4 /dev/loop1 /dev/loop2 /dev/loop3 /dev/loop4
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 42
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
8
STEP 8 OF 9
Simulate a failure and rebuild, watching resync
$ mdadm /dev/md1 --fail /dev/loop2 --remove /dev/loop2
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 43
LAB 2 · Storage Deployment: RAID 0/1/5/6/1
Storage Deployment: RAID 0/1/5/6/10 with mdadm
9
STEP 9 OF 9
Compare hardware RAID vs software RAID trade-offs
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 44
LAB 2 · VERIFY
Storage Deployment: RAID 0/1/5/6/10 with mdadm
✅ Test it
The learner verifies success by reading the array status in /proc/mdstat and confirming the capacity and fault-tolerance formula for each level.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 45
TOPIC 01 · HANDS-ON
LVM Provisioning and Capacity Planning
LAB 3
The learner provisions storage through the PV to VG to LV model, extends a volume online, adds swap and takes a point-in-time snapshot.
You'll build
An LVM volume group with web, database and swap volumes plus a live snapshot.
Tools: lvm2, mkfs.ext4, mkfs.xfs
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 46
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
1
STEP 1 OF 9
Install lvm2
$ apt update && apt install -y lvm2
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 47
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
2
STEP 2 OF 9
Create four loopback disks
$ for i in 1 2 3 4; do truncate -s 500M disk$i.img; losetup /dev/loop$i disk$i.img; done
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 48
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
3
STEP 3 OF 9
Create physical volumes and a volume group
$ vgcreate vg_data /dev/loop1 /dev/loop2 /dev/loop3
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 49
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
4
STEP 4 OF 9
Create logical volumes for web and database
$ lvcreate -L 800M -n lv_web vg_data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 50
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
5
STEP 5 OF 9
Extend the DB volume online (add PV, grow LV, grow FS)
$ lvextend -L +400M /dev/vg_data/lv_db
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 51
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
6
STEP 6 OF 9
Grow the XFS filesystem online
$ xfs_growfs /srv/db
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 52
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
7
STEP 7 OF 9
Create a dedicated swap LV
$ lvcreate -L 200M -n lv_swap vg_data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 53
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
8
STEP 8 OF 9
Take a point-in-time snapshot of a live volume
$ lvcreate -L 100M -s -n lv_web_snap /dev/vg_data/lv_web
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 54
LAB 3 · LVM Provisioning and Capacity Plan
LVM Provisioning and Capacity Planning
9
STEP 9 OF 9
Report capacity vs utilisation as a baseline
$ vgs --units g -o vg_name,vg_size,vg_free
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 55
LAB 3 · VERIFY
LVM Provisioning and Capacity Planning
✅ Test it
The learner verifies success by confirming the extended volume grew online and the snapshot restores a deleted file.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 56
TOPIC 01 · HANDS-ON
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
LAB 4
The learner exports file-level NFS and CIFS shares and builds a block-level iSCSI target, then connects an initiator and formats the LUN as a disk.
You'll build
A working NFS share, a Samba/CIFS share and a mounted iSCSI SAN LUN.
Tools: nfs-kernel-server, samba, tgt, open-iscsi
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 57
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
1
STEP 1 OF 9
Install the NAS and SAN packages
$ apt update && apt install -y nfs-kernel-server nfs-common tgt open-iscsi samba
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 58
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
2
STEP 2 OF 9
Export an NFS share (file-level NAS)
$ echo "/srv/nfs/share 127.0.0.1(rw,sync,no_subtree_check,no_root_squash)" >> /etc/exports
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 59
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
3
STEP 3 OF 9
Mount the NFS share as a client
$ mount -t nfs 127.0.0.1:/srv/nfs/share /mnt/nas
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 60
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
4
STEP 4 OF 9
Create a CIFS/SMB share and browse it
$ smbclient -L //127.0.0.1 -N
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 61
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
5
STEP 5 OF 9
Build an iSCSI target with a 500 MB LUN
$ systemctl restart tgt
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 62
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
6
STEP 6 OF 9
Discover and log in to the iSCSI target
$ iscsiadm -m discovery -t st -p 127.0.0.1
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 63
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
7
STEP 7 OF 9
Log in to the iSCSI node
$ iscsiadm -m node --login
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 64
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
8
STEP 8 OF 9
Format and mount the new SAN LUN as a local disk
$ mkfs.ext4 /dev/$NEW
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 65
LAB 4 · Shared Storage: NAS (NFS/CIFS) and
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
9
STEP 9 OF 9
Compare NAS vs SAN vs Fibre Channel/FCoE
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 66
LAB 4 · VERIFY
Shared Storage: NAS (NFS/CIFS) and SAN (iSCSI)
✅ Test it
The learner verifies success by reading files over the NFS/CIFS mounts and confirming a new /dev/sdX LUN appears from the iSCSI target and mounts.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 67
TOPIC 01 · HANDS-ON
Out-of-Band Management, BIOS/UEFI, and Firmware
LAB 5
The learner inspects BIOS/UEFI from the OS, practises the efibootmgr and ipmitool workflows, and walks the fwupd firmware-upgrade and hot-swap checklists.
You'll build
A firmware/BIOS inventory and a documented OOB management and hot-swap workflow.
Tools: ipmitool, fwupd, efibootmgr, dmidecode
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 68
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
1
STEP 1 OF 9
Install the OOB and firmware tools
$ apt update && apt install -y ipmitool fwupd efibootmgr dmidecode
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 69
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
2
STEP 2 OF 9
Inventory BIOS/UEFI from the running OS
$ dmidecode -t bios
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 70
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
3
STEP 3 OF 9
Confirm UEFI vs legacy BIOS boot mode
$ [ -d /sys/firmware/efi ] && echo "Booted in UEFI mode" || echo "Booted in legacy BIOS mode"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 71
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
4
STEP 4 OF 9
List UEFI boot entries
$ efibootmgr -v
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 72
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
5
STEP 5 OF 9
Practise the IPMI/BMC chassis-status pattern
$ ipmitool -H bmc.example.com -U admin -P 'CHANGEME' chassis status
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 73
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
6
STEP 6 OF 9
List which firmware is installed with fwupd
$ fwupdmgr get-devices
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 74
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
7
STEP 7 OF 9
Check for available firmware updates
$ fwupdmgr get-updates
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 75
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
8
STEP 8 OF 9
Walk the four local-admin paths (crash cart, KVM, serial, virtual console)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 76
LAB 5 · Out-of-Band Management, BIOS/UEFI,
Out-of-Band Management, BIOS/UEFI, and Firmware
9
STEP 9 OF 9
Walk the hot-swap pre-swap checklist for drives, PSUs and fans
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 77
LAB 5 · VERIFY
Out-of-Band Management, BIOS/UEFI, and Firmware
✅ Test it
The learner verifies success by reading the BIOS version and boot mode and mapping each ipmitool command to its Server+ OOB sub-objective.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 78
TOPIC RECAP
Recap — Server Hardware Installation and Management
• You can now: 1.1 Install physical hardware
• You can now: 1.2 Deploy and manage storage (RAID levels, JBOD, capacity planning)
• You can now: 1.2/2.1/2.3 Capacity planning and logical volume management
• You can now: 1.2 Shared storage: NAS (NFS, CIFS), SAN (iSCSI)
• You can now: 1.3 Perform server hardware maintenance (OOB, BIOS/UEFI, firmware, hot-swap)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 79
TOPIC 02
Server Administration
OS install & file systems · networking · roles, HA, virtualization, scripting & assets
02
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 80
EXAM WEIGHTING 30%
Key Concepts — Server Administration
1
OS installation
Attended, unattended, scripted and image-based installs; partition schemes (MBR vs. GPT); file systems (ext4, XFS, ZFS, NTFS).
2
Network services
IPv4/IPv6 addressing and subnetting, DNS, DHCP, FQDN, VLANs and default gateways for a server.
3
Server roles & monitoring
Web, file, database, directory and print roles; performance baselining, metrics and thresholds; data migration.
4
High availability
Clustering, load balancing, NIC teaming and failover to remove single points of failure.
5
Virtualization & cloud
Host vs. guest, hypervisor types, resource allocation and over-commit; IaaS/PaaS/SaaS and public/private/hybrid models.
6
Scripting & asset management
Variables, loops and conditionals for common server tasks; documentation, lifecycle and secure asset storage.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 81
WHAT YOU'LL DO
Hands-On Labs — Server Administration
Labs 6–9
• Installing a Server OS (Unattended / Scripted)
• Partition and Volume Types, File Systems
• IP, VLAN, DNS, DHCP, FQDN, and Hosts File
• Server Firewall and Port Management
Labs 10–13
• Server Roles: Web, File, and Database
• Directory Services with OpenLDAP
• Performance Monitoring, Baselining, Event Logs
• Data Migration and Transfer
Labs 14–17
• High Availability: Clustering, Load Balancing, NIC Teaming
• Virtualization with KVM / QEMU
• Scripting Basics for Server Administration
• Asset Management, Documentation, and Licensing
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 82
TOPIC 02 · HANDS-ON
Installing a Server OS (Unattended / Scripted)
LAB 6
The learner validates minimum specs and the HCL, builds a cloud-init autoinstall seed.iso, captures a golden image and walks the P2V conversion workflow.
You'll build
A cloud-init autoinstall seed.iso and a golden-image tarball for template deployment.
Tools: debootstrap, cloud-init, genisoimage, qemu-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 83
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
1
STEP 1 OF 9
Install the OS-deployment tools
$ apt update && apt install -y debootstrap cloud-init genisoimage qemu-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 84
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
2
STEP 2 OF 9
Confirm minimum OS requirements (CPU, RAM, disk)
$ lscpu | grep -E "Architecture|CPU\(s\)"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 85
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
3
STEP 3 OF 9
Do an HCL check on CPU, NIC and storage controller
$ echo "NIC: $(lspci | grep -i ether)"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 86
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
4
STEP 4 OF 9
Build a minimal cloud-init autoinstall config
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 87
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
5
STEP 5 OF 9
Package the config into a NoCloud seed ISO
$ genisoimage -output seed.iso -volid cidata -joliet -rock user-data meta-data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 88
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
6
STEP 6 OF 9
Capture a golden image of the root filesystem
$ tar --one-file-system --exclude=/proc --exclude=/sys --exclude=/dev --exclude=/mnt -czf /srv/golden.tgz / 2>/dev/null
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 89
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
7
STEP 7 OF 9
Build a template root filesystem with debootstrap
$ debootstrap --variant=minbase jammy /srv/template http://archive.ubuntu.com/ubuntu/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 90
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
8
STEP 8 OF 9
Create a destination image shape for P2V conversion
$ qemu-img create -f qcow2 /srv/converted.qcow2 5G
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 91
LAB 6 · Installing a Server OS (Unattended
Installing a Server OS (Unattended / Scripted)
9
STEP 9 OF 9
Compare GUI vs Core vs Bare metal vs Virtualized vs Remote installs
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 92
LAB 6 · VERIFY
Installing a Server OS (Unattended / Scripted)
✅ Test it
The learner verifies success by confirming the seed.iso is built and the golden-image tarball and debootstrap template are deployable filesystems.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 93
TOPIC 02 · HANDS-ON
Partition and Volume Types, File Systems
LAB 7
The learner partitions a disk with MBR then GPT, formats ext4/XFS/ZFS, persists mounts by UUID and converts MBR to GPT non-destructively.
You'll build
A GPT-partitioned disk with ext4, XFS and ZFS filesystems and a UUID-based fstab entry.
Tools: parted, gdisk, e2fsprogs, xfsprogs, zfsutils-linux
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 94
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
1
STEP 1 OF 9
Install the partitioning and filesystem tools
$ apt update && apt install -y parted gdisk e2fsprogs xfsprogs zfsutils-linux ntfs-3g
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 95
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
2
STEP 2 OF 9
Create a 4G loopback disk to partition
$ losetup -P /dev/loop10 /srv/disk.img
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 96
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
3
STEP 3 OF 9
Create an MBR (msdos) partition table
$ parted -s /dev/loop10 mklabel msdos
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 97
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
4
STEP 4 OF 9
Switch the disk to a GPT partition table
$ parted -s /dev/loop10 mklabel gpt
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 98
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
5
STEP 5 OF 9
Format the ext4 partition
$ mkfs.ext4 /dev/loop10p1
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 99
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
6
STEP 6 OF 9
Create a ZFS pool on a partition
$ zpool create -f tank /dev/loop10p3
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 100
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
7
STEP 7 OF 9
Compare the five Server+ filesystems (ext4, NTFS, VMFS, ReFS, ZFS)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 101
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
8
STEP 8 OF 9
Persist a mount by UUID in /etc/fstab
$ echo "UUID=$UUID /mnt/p1 ext4 defaults,noatime 0 2" | tee -a /etc/fstab
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 102
LAB 7 · Partition and Volume Types, File S
Partition and Volume Types, File Systems
9
STEP 9 OF 9
Convert MBR to GPT non-destructively with gdisk
$ gdisk -l /dev/loop10 | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 103
LAB 7 · VERIFY
Partition and Volume Types, File Systems
✅ Test it
The learner verifies success by printing the partition table with parted/gdisk and confirming the UUID-based fstab mount survives mount -a.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 104
TOPIC 02 · HANDS-ON
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
LAB 8
The learner configures a static IP and gateway, tags a VLAN, builds a BIND9 zone with A records and a DHCP scope, and simulates APIPA.
You'll build
A configured static IP with VLAN, a BIND9 zone serving an FQDN and a validated DHCP scope.
Tools: iproute2, bind9, dnsutils, isc-dhcp-server
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 105
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
1
STEP 1 OF 9
Install the networking service packages
$ apt update && apt install -y iproute2 vlan bind9 bind9utils dnsutils isc-dhcp-server
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 106
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
2
STEP 2 OF 9
Inspect IP configuration, routes and MAC addresses
$ ip -c addr
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 107
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
3
STEP 3 OF 9
Configure a static IP and default gateway
$ ip addr add 10.99.99.10/24 dev eth0
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 108
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
4
STEP 4 OF 9
Tag VLAN 20 on a single NIC with 802.1Q
$ ip link add link eth0 name eth0.20 type vlan id 20
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 109
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
5
STEP 5 OF 9
Review RFC 1918 private ranges and APIPA
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 110
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
6
STEP 6 OF 9
Build a BIND9 zone with A records and restart
$ systemctl restart bind9
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 111
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
7
STEP 7 OF 9
Resolve the FQDN against the local server
$ dig @127.0.0.1 web.lab.local +short
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 112
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
8
STEP 8 OF 9
Add a hosts-file override that beats DNS
$ echo "10.99.99.50 app.lab.local app" >> /etc/hosts
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 113
LAB 8 · IP, VLAN, DNS, DHCP, FQDN, and Hos
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
9
STEP 9 OF 9
Validate an ISC DHCP scope config
$ dhcpd -t -cf /etc/dhcp/dhcpd.conf && echo "Config OK"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 114
LAB 8 · VERIFY
IP, VLAN, DNS, DHCP, FQDN, and Hosts File
✅ Test it
The learner verifies success by resolving web.lab.local through BIND9 and confirming the DHCP config passes validation.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 115
TOPIC 02 · HANDS-ON
Server Firewall and Port Management
LAB 9
The learner memorises the well-known ports, applies a default-deny UFW policy, translates it to raw nftables and audits listening vs reachable vs permitted.
You'll build
A default-deny firewall permitting only SSH/HTTP/HTTPS with source-restricted rules.
Tools: ufw, nftables, nginx, nmap
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 116
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
1
STEP 1 OF 9
Install the firewall and scan tools
$ apt update && apt install -y ufw nftables nginx nmap
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 117
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
2
STEP 2 OF 9
Review the well-known server port table
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 118
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
3
STEP 3 OF 9
Start a service and observe its open port
$ ss -tlnp | grep nginx
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 119
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
4
STEP 4 OF 9
Apply a default-deny UFW policy with explicit allows
$ ufw default deny incoming
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 120
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
5
STEP 5 OF 9
Allow SSH, HTTP and HTTPS
$ ufw allow 22/tcp comment 'SSH admin'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 121
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
6
STEP 6 OF 9
Confirm the policy with nmap
$ nmap -p 22,23,25,80,443,3306 127.0.0.1
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 122
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
7
STEP 7 OF 9
Write the equivalent rule in raw nftables
$ nft add rule inet filter input tcp dport 8080 accept
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 123
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
8
STEP 8 OF 9
Add a source-restricted rule for MySQL
$ ufw allow from 10.99.99.0/24 to any port 3306 proto tcp comment 'MySQL app tier'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 124
LAB 9 · Server Firewall and Port Managemen
Server Firewall and Port Management
9
STEP 9 OF 9
Run the 3-view audit: listening, reachable, permitted
$ ss -tulnp
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 125
LAB 9 · VERIFY
Server Firewall and Port Management
✅ Test it
The learner verifies success by confirming nmap sees only the allowed ports open and the ss, nmap and ufw views agree.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 126
TOPIC 02 · HANDS-ON
Server Roles: Web, File, and Database
LAB 10
The learner stands up nginx, Samba and MariaDB end-to-end on one host, applies resource limits and documents a role inventory.
You'll build
A single host serving web, file and database roles with per-role resource limits.
Tools: nginx, samba, mariadb-server, curl
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 127
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
1
STEP 1 OF 8
Install the three role packages
$ apt update && apt install -y nginx samba mariadb-server curl cifs-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
126

## Slide 128
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
2
STEP 2 OF 8
Start nginx and serve a page (web role)
$ curl -s http://127.0.0.1/ | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
127

## Slide 129
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
3
STEP 3 OF 8
Add a name-based virtual host
$ ln -sf /etc/nginx/sites-available/site1 /etc/nginx/sites-enabled/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
128

## Slide 130
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
4
STEP 4 OF 8
Create a Samba user and share (file role)
$ (echo 'P@ssw0rd!'; echo 'P@ssw0rd!') | smbpasswd -s -a alice
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
129

## Slide 131
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
5
STEP 5 OF 8
Connect to the Samba share
$ smbclient //127.0.0.1/share -U alice%P@ssw0rd! -c 'ls'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
130

## Slide 132
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
6
STEP 6 OF 8
Create a MariaDB database and least-privilege user (database role)
$ mysql -e "CREATE DATABASE appdb;"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
131

## Slide 133
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
7
STEP 7 OF 8
Apply systemd resource limits so roles don't starve each other
$ systemctl set-property mariadb.service MemoryMax=512M CPUQuota=80%
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
132

## Slide 134
LAB 10 · Server Roles: Web, File, and Datab
Server Roles: Web, File, and Database
8
STEP 8 OF 8
Document the role inventory to a file
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
133

## Slide 135
LAB 10 · VERIFY
Server Roles: Web, File, and Database
✅ Test it
The learner verifies success by getting a page from nginx, listing the Samba share and running a SELECT against MariaDB.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
134

## Slide 136
TOPIC 02 · HANDS-ON
Directory Services with OpenLDAP
LAB 11
The learner installs OpenLDAP, builds an OU/user/group tree, binds as a user and adds a group-based delegation ACL.
You'll build
An OpenLDAP directory with an OU structure, users, groups and a delegation ACL.
Tools: slapd, ldap-utils, ldapscripts
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
135

## Slide 137
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
1
STEP 1 OF 9
Install and preseed slapd non-interactively
$ DEBIAN_FRONTEND=noninteractive apt install -y slapd ldap-utils ldapscripts
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
136

## Slide 138
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
2
STEP 2 OF 9
Verify the directory is running
$ ldapsearch -x -H ldap://127.0.0.1 -b "dc=lab,dc=local" -s base "(objectclass=*)" namingContexts
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
137

## Slide 139
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
3
STEP 3 OF 9
Create the people and groups OUs
$ ldapadd -x -D "cn=admin,dc=lab,dc=local" -w LabAdmin1! -f /tmp/ou.ldif
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
138

## Slide 140
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
4
STEP 4 OF 9
Add user accounts
$ ldapadd -x -D "cn=admin,dc=lab,dc=local" -w LabAdmin1! -f /tmp/users.ldif
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
139

## Slide 141
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
5
STEP 5 OF 9
Set a user password
$ ldappasswd -x -D "cn=admin,dc=lab,dc=local" -w LabAdmin1! -s 'AlicePass!' "uid=alice,ou=people,dc=lab,dc=local"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
140

## Slide 142
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
6
STEP 6 OF 9
Create groups and assign membership
$ ldapadd -x -D "cn=admin,dc=lab,dc=local" -w LabAdmin1! -f /tmp/groups.ldif
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
141

## Slide 143
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
7
STEP 7 OF 9
Bind as a user and confirm identity
$ ldapwhoami -x -D "uid=alice,ou=people,dc=lab,dc=local" -w 'AlicePass!'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
142

## Slide 144
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
8
STEP 8 OF 9
Add a group-based delegation ACL
$ ldapmodify -Y EXTERNAL -H ldapi:/// -f /tmp/acl.ldif
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
143

## Slide 145
LAB 11 · Directory Services with OpenLDAP
Directory Services with OpenLDAP
9
STEP 9 OF 9
Map the concepts to Active Directory (OU=scope, group=role, ACL=delegation)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
144

## Slide 146
LAB 11 · VERIFY
Directory Services with OpenLDAP
✅ Test it
The learner verifies success by binding as alice and searching entries under ou=people.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
145

## Slide 147
TOPIC 02 · HANDS-ON
Performance Monitoring, Baselining, Event Logs
LAB 12
The learner captures CPU/memory/disk/network baselines, inspects and rotates event logs, and wires threshold alerting with Prometheus node_exporter.
You'll build
A saved performance baseline file and a node_exporter metrics endpoint for alerting.
Tools: sysstat, htop, iotop, fio, prometheus-node-exporter
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
146

## Slide 148
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
1
STEP 1 OF 8
Install the monitoring tools and enable sysstat
$ apt update && apt install -y sysstat htop iotop fio prometheus-node-exporter
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
147

## Slide 149
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
2
STEP 2 OF 8
Read uptime and load averages
$ uptime
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
148

## Slide 150
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
3
STEP 3 OF 8
Capture a CPU baseline
$ mpstat 1 5
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
149

## Slide 151
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
4
STEP 4 OF 8
Capture a memory baseline
$ sar -r 1 5
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
150

## Slide 152
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
5
STEP 5 OF 8
Generate I/O load and measure IOPS and latency
$ iostat -xz 1 5
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
151

## Slide 153
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
6
STEP 6 OF 8
Save a combined baseline file for later diffing
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
152

## Slide 154
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
7
STEP 7 OF 8
Inspect event logs and configure rotation/retention
$ journalctl --since "1 hour ago" -p err
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
153

## Slide 155
LAB 12 · Performance Monitoring, Baselining
Performance Monitoring, Baselining, Event Logs
8
STEP 8 OF 8
Expose metrics with node_exporter for thresholds/alerting
$ curl -s http://127.0.0.1:9100/metrics | grep -E 'node_cpu_seconds_total|node_memory_MemAvailable|node_filesystem_free' | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
154

## Slide 156
LAB 12 · VERIFY
Performance Monitoring, Baselining, Event Logs
✅ Test it
The learner verifies success by producing a baseline file and confirming node_exporter serves the CPU, memory and filesystem metrics.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
155

## Slide 157
TOPIC 02 · HANDS-ON
Data Migration and Transfer
LAB 13
The learner transfers data with rsync, SCP and SFTP, applies fast-copy techniques and reviews exfiltration controls including bandwidth caps.
You'll build
A mirrored dataset transferred with rsync/SCP/SFTP plus egress controls.
Tools: rsync, openssh-client, lftp, pv
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
156

## Slide 158
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
1
STEP 1 OF 9
Install the transfer tools and start ssh
$ apt update && apt install -y rsync openssh-client openssh-server lftp pv
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
157

## Slide 159
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
2
STEP 2 OF 9
Set up source and destination trees
$ for i in $(seq 1 50); do dd if=/dev/urandom of=/srv/src/file$i.bin bs=1K count=$((RANDOM%200+10)) 2>/dev/null; done
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
158

## Slide 160
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
3
STEP 3 OF 9
Mirror with rsync (archive, delta, delete)
$ rsync -avh /srv/src/ /srv/dst/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
159

## Slide 161
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
4
STEP 4 OF 9
Rsync over SSH to a remote host
$ rsync -avzh -e ssh /srv/src/ user@remote:/srv/dst/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
160

## Slide 162
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
5
STEP 5 OF 9
Copy with SCP (simple, no resume)
$ scp -r /srv/src/ root@127.0.0.1:/srv/dst-scp/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
161

## Slide 163
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
6
STEP 6 OF 9
Transfer interactively over SFTP
$ sftp root@127.0.0.1
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
162

## Slide 164
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
7
STEP 7 OF 9
Compare cross-OS choices including Windows Robocopy
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
163

## Slide 165
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
8
STEP 8 OF 9
Fast-copy a large file showing throughput
$ pv /srv/src/file1.bin > /srv/dst/file1.bin
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
164

## Slide 166
LAB 13 · Data Migration and Transfer
Data Migration and Transfer
9
STEP 9 OF 9
Apply a bandwidth cap to limit exfiltration
$ rsync -avh --bwlimit=1024 /srv/src/ user@remote:/srv/dst/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
165

## Slide 167
LAB 13 · VERIFY
Data Migration and Transfer
✅ Test it
The learner verifies success by confirming the destination mirrors the source and understands when to use SCP vs SFTP vs rsync.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
166

## Slide 168
TOPIC 02 · HANDS-ON
High Availability: Clustering, Load Balancing, NIC Teaming
LAB 14
The learner builds an HAProxy round-robin load balancer over two backends, observes failover and failback, and configures keepalived VRRP and NIC bonding.
You'll build
An HAProxy load balancer with health checks plus keepalived and NIC-bond configs.
Tools: haproxy, keepalived, nginx, ifenslave
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
167

## Slide 169
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
1
STEP 1 OF 9
Install the HA packages
$ apt update && apt install -y haproxy keepalived nginx ifenslave apache2-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
168

## Slide 170
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
2
STEP 2 OF 9
Start two backend web servers on different ports
$ nohup python3 -m http.server 8001 --directory /srv/back1 >/tmp/b1.log 2>&1 &
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
169

## Slide 171
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
3
STEP 3 OF 9
Configure HAProxy round-robin with health checks
$ systemctl restart haproxy
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
170

## Slide 172
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
4
STEP 4 OF 9
Test round-robin distribution across backends
$ for i in 1 2 3 4; do curl -s 127.0.0.1:8080; done
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
171

## Slide 173
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
5
STEP 5 OF 9
Switch the algorithm to least-conn
$ sed -i 's/balance roundrobin/balance leastconn/' /etc/haproxy/haproxy.cfg
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
172

## Slide 174
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
6
STEP 6 OF 9
Kill a backend to observe failover
$ kill $(lsof -ti :8001) || pkill -f '8001'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
173

## Slide 175
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
7
STEP 7 OF 9
Configure keepalived VRRP heartbeat for a floating VIP
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
174

## Slide 176
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
8
STEP 8 OF 9
Configure NIC bonding (active-backup vs 802.3ad LACP)
$ modprobe bonding mode=active-backup miimon=100
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
175

## Slide 177
LAB 14 · High Availability: Clustering, Loa
High Availability: Clustering, Load Balancing, NIC Teaming
9
STEP 9 OF 9
Review the cluster-aware patching procedure
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
176

## Slide 178
LAB 14 · VERIFY
High Availability: Clustering, Load Balancing, NIC Teaming
✅ Test it
The learner verifies success by seeing traffic alternate across backends and only the surviving backend answer after a failover.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
177

## Slide 179
TOPIC 02 · HANDS-ON
Virtualization with KVM / QEMU
LAB 15
The learner creates a thin-provisioned qcow2 disk, defines a VM with virt-install, inspects virtual networking and adds a second virtual switch.
You'll build
A defined KVM VM with a qcow2 disk and a second isolated virtual switch.
Tools: qemu-kvm, libvirt-daemon-system, virtinst, bridge-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
178

## Slide 180
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
1
STEP 1 OF 9
Install the virtualization stack and start libvirtd
$ apt update && apt install -y qemu-system-x86 qemu-utils libvirt-daemon-system virtinst bridge-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
179

## Slide 181
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
2
STEP 2 OF 9
Check whether the host CPU supports hardware virt
$ egrep -c '(vmx|svm)' /proc/cpuinfo
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
180

## Slide 182
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
3
STEP 3 OF 9
Create a thin-provisioned qcow2 virtual disk
$ qemu-img create -f qcow2 /var/lib/libvirt/images/vm1.qcow2 5G
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
181

## Slide 183
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
4
STEP 4 OF 9
Define a VM mapping each flag to objective 2.5
$ virsh list --all
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
182

## Slide 184
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
5
STEP 5 OF 9
Inspect the default virtual network and virbr0
$ virsh net-dumpxml default
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
183

## Slide 185
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
6
STEP 6 OF 9
Compare bridged vs NAT vs isolated networking
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
184

## Slide 186
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
7
STEP 7 OF 9
Add and start a second virtual switch
$ virsh net-start internal
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
185

## Slide 187
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
8
STEP 8 OF 9
Review CPU/memory/disk/NIC overprovisioning rules
$ nproc
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
186

## Slide 188
LAB 15 · Virtualization with KVM / QEMU
Virtualization with KVM / QEMU
9
STEP 9 OF 9
Compare public, private and hybrid cloud models
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
187

## Slide 189
LAB 15 · VERIFY
Virtualization with KVM / QEMU
✅ Test it
The learner verifies success by confirming the qcow2 disk is thin-provisioned and the second virtual network starts and appears in virsh net-list.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
188

## Slide 190
TOPIC 02 · HANDS-ON
Scripting Basics for Server Administration
LAB 16
The learner writes Bash scripts covering variables, data types, conditionals, loops and real admin tasks like service management and bulk account creation.
You'll build
A set of Bash scripts for service checks, bulk account creation and host bootstrap.
Tools: bash, coreutils, systemctl
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
189

## Slide 191
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
1
STEP 1 OF 8
Review the four script types and their platforms
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
190

## Slide 192
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
2
STEP 2 OF 8
Write a script using variables, comments and environment exports
$ chmod +x 01-basics.sh && ./01-basics.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
191

## Slide 193
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
3
STEP 3 OF 8
Use integers, strings and arrays
$ chmod +x 02-types.sh && ./02-types.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
192

## Slide 194
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
4
STEP 4 OF 8
Write a disk-usage conditional with comparators
$ chmod +x 03-conditionals.sh && ./03-conditionals.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
193

## Slide 195
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
5
STEP 5 OF 8
Write for and while loops
$ chmod +x 04-loops.sh && ./04-loops.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
194

## Slide 196
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
6
STEP 6 OF 8
Write a service-management task script
$ chmod +x 05-services.sh && ./05-services.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
195

## Slide 197
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
7
STEP 7 OF 8
Write a bulk account-creation task script
$ chmod +x 06-accounts.sh && ./06-accounts.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
196

## Slide 198
LAB 16 · Scripting Basics for Server Admini
Scripting Basics for Server Administration
8
STEP 8 OF 8
Write a bootstrap script with set -euo pipefail discipline
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
197

## Slide 199
LAB 16 · VERIFY
Scripting Basics for Server Administration
✅ Test it
The learner verifies success by running each script and confirming the service, account and bootstrap tasks produce the expected output.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
198

## Slide 200
TOPIC 02 · HANDS-ON
Asset Management, Documentation, and Licensing
LAB 17
The learner scripts asset discovery, captures an as-built config set, reviews BIA-driven metrics and the licensing model table, and validates a license count.
You'll build
A discovered asset CSV, an as-built config snapshot and a license-count report.
Tools: dmidecode, coreutils, spreadsheet
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
199

## Slide 201
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
1
STEP 1 OF 8
Auto-discover the asset details into a CSV
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
200

## Slide 202
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
2
STEP 2 OF 8
Review the asset life-cycle stages
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
201

## Slide 203
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
3
STEP 3 OF 8
Capture the running config as an as-built doc set
$ systemctl list-units --type=service --state=running > services.txt
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
202

## Slide 204
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
4
STEP 4 OF 8
Review BIA-driven metrics (MTBF, MTTR, RPO, RTO, SLA, uptime)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
203

## Slide 205
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
5
STEP 5 OF 8
Draft a change-management entry template
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
204

## Slide 206
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
6
STEP 6 OF 8
Restrict permissions on sensitive documentation
$ chmod 750 /root/asbuilt
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
205

## Slide 207
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
7
STEP 7 OF 8
Review the Server+ licensing model cheat sheet
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
206

## Slide 208
LAB 17 · Asset Management, Documentation, a
Asset Management, Documentation, and Licensing
8
STEP 8 OF 8
Run a license-count validation script for true-up
$ chmod +x /root/license-count.sh && /root/license-count.sh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
207

## Slide 209
LAB 17 · VERIFY
Asset Management, Documentation, and Licensing
✅ Test it
The learner verifies success by producing the asset CSV, the as-built config files and a socket/core/vCPU count for a true-up.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
208

## Slide 210
TOPIC RECAP
Recap — Server Administration
• You can now: 2.1 Install server operating systems
• You can now: 2.1 Partition/volume types (GPT vs MBR, LVM) and file systems
• You can now: 2.2 Configure servers to use network infrastructure services
• You can now: 2.2 Firewall, Ports
• You can now: 2.3 Server roles requirements (Web, File, Database)
• You can now: 2.3/3.3 Directory connectivity, scope-based delegation
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
209

## Slide 211
TOPIC 03
Security and Disaster Recovery
Data & physical security · IAM · mitigation & hardening · decommissioning · backup & DR
03
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
210

## Slide 212
EXAM WEIGHTING 24%
Key Concepts — Security and Disaster Recovery
1
Data security
Encryption at rest (LUKS/BitLocker) and in transit (TLS/SSH); retention policies and the data lifecycle.
2
Physical security
Access controls, mantraps, badge/biometric systems, cameras and environmental controls for the server room.
3
Identity & access management
User accounts, groups, RBAC, least privilege, MFA and permission management.
4
Mitigation & hardening
Malware prevention, DLP, SIEM; OS updates, disabling unused services and host-based hardening.
5
Decommissioning
NIST 800-88 media sanitization — clear, purge, destroy; recycling and asset disposal records.
6
Backup & disaster recovery
Full/incremental/differential backups, the 3-2-1 rule, snapshots, replication and site failover; RPO and RTO.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
211

## Slide 213
WHAT YOU'LL DO
Hands-On Labs — Security and Disaster Recovery
Labs 18–21
• Data at Rest (LUKS) and Data in Transit (TLS/SSH)
• Physical and Environmental Security Walk-Through
• Identity & Access Management for Server Administration
• Multi-Factor Authentication with TOTP (PAM)
Labs 22–25
• Auditing, Logging, and SIEM Basics
• OS and Application Hardening
• Patch and Update Management
• Secure Decommissioning and Media Destruction
Labs 26–27
• Backup Strategy: Full, Incremental, Differential, Snapshot
• Disaster Recovery: Replication and Site Failover
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
212

## Slide 214
TOPIC 03 · HANDS-ON
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
LAB 18
The learner encrypts a volume with LUKS, proves the ciphertext is unreadable, serves TLS with a self-signed cert and hardens SSH.
You'll build
A LUKS-encrypted volume and a TLS-enabled nginx site with hardened SSH.
Tools: cryptsetup, openssl, openssh-server
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
213

## Slide 215
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
1
STEP 1 OF 9
Install the encryption tools
$ apt update && apt install -y cryptsetup openssl openssh-server
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
214

## Slide 216
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
2
STEP 2 OF 9
Format a volume at rest with LUKS
$ cryptsetup luksFormat /dev/loop20 --batch-mode --key-file=<(echo -n 'LabPass!1')
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
215

## Slide 217
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
3
STEP 3 OF 9
Open, format and mount the encrypted volume
$ cryptsetup luksOpen /dev/loop20 secret --key-file=<(echo -n 'LabPass!1')
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
216

## Slide 218
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
4
STEP 4 OF 9
Close it and prove the raw bytes are unreadable
$ strings /srv/secret.img | grep financials || echo "no plaintext visible — at-rest encryption works"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
217

## Slide 219
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
5
STEP 5 OF 9
Inspect the cipher and LUKS header
$ cryptsetup luksDump /dev/loop20 | head -30
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
218

## Slide 220
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
6
STEP 6 OF 9
Generate a self-signed TLS cert and serve HTTPS
$ openssl req -x509 -newkey rsa:2048 -nodes -keyout /etc/ssl/private/lab.key -out /etc/ssl/certs/lab.crt -subj "/CN=lab.local" -days 365
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
219

## Slide 221
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
7
STEP 7 OF 9
Verify the negotiated TLS protocol and cipher
$ echo | openssl s_client -connect 127.0.0.1:443 -servername lab.local 2>/dev/null | grep -E "Protocol|Cipher\s+:"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
220

## Slide 222
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
8
STEP 8 OF 9
Review SSH hardening lines and BIOS/GRUB passwords
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
221

## Slide 223
LAB 18 · Data at Rest (LUKS) and Data in Tr
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
9
STEP 9 OF 9
Map a retention policy to data classification
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
222

## Slide 224
LAB 18 · VERIFY
Data at Rest (LUKS) and Data in Transit (TLS/SSH)
✅ Test it
The learner verifies success by confirming no plaintext is recoverable from the closed LUKS image and TLS 1.2/1.3 is negotiated.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
223

## Slide 225
TOPIC 03 · HANDS-ON
Physical and Environmental Security Walk-Through
LAB 19
The learner inspects environmental sensors the OS can see and walks the physical access-control layers, lock types, environmental controls and a security checklist.
You'll build
A completed physical-security audit checklist for a server room.
Tools: lm-sensors, smartmontools
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
224

## Slide 226
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
1
STEP 1 OF 9
Install the sensor tools
$ apt update && apt install -y lm-sensors smartmontools
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
225

## Slide 227
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
2
STEP 2 OF 9
Review the physical access-control layers (defence in depth)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
226

## Slide 228
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
3
STEP 3 OF 9
Review lock and authenticator types (RFID, biometric)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
227

## Slide 229
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
4
STEP 4 OF 9
Inspect environmental sensors the OS exposes
$ sensors 2>/dev/null | head -30
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
228

## Slide 230
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
5
STEP 5 OF 9
Read drive temperature via SMART
$ smartctl -a /dev/sda 2>/dev/null | grep -i temperature | head -3
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
229

## Slide 231
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
6
STEP 6 OF 9
Review cameras and guards as detective controls
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
230

## Slide 232
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
7
STEP 7 OF 9
Map the concentric data-centre security zones
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
231

## Slide 233
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
8
STEP 8 OF 9
Review the mantrap defence against tailgating
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
232

## Slide 234
LAB 19 · Physical and Environmental Securit
Physical and Environmental Security Walk-Through
9
STEP 9 OF 9
Complete the physical-security audit checklist
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
233

## Slide 235
LAB 19 · VERIFY
Physical and Environmental Security Walk-Through
✅ Test it
The learner verifies success by reading available environmental sensor data and completing the physical-security checklist.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
234

## Slide 236
TOPIC 03 · HANDS-ON
Identity & Access Management for Server Administration
LAB 20
The learner builds RBAC groups with segregation of duties, delegates via sudoers, enforces password policy and lockout, and audits access.
You'll build
Three RBAC roles with scoped sudoers rules, password policy and audit checks.
Tools: sudo, libpam-pwquality, chage, setfacl
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
235

## Slide 237
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
1
STEP 1 OF 9
Install the IAM tools
$ apt update && apt install -y sudo libpam-pwquality
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
236

## Slide 238
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
2
STEP 2 OF 9
Create three role groups and users (segregation of duties)
$ useradd -m -G sysops alice && echo 'alice:AlicePass!1' | chpasswd
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
237

## Slide 239
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
3
STEP 3 OF 9
Delegate scoped commands per role via sudoers
$ visudo -c
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
238

## Slide 240
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
4
STEP 4 OF 9
Test that each role can only run its own commands
$ sudo -u bob -i bash -c 'sudo systemctl restart mariadb && echo bob-ok'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
239

## Slide 241
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
5
STEP 5 OF 9
Enforce password length and complexity policy
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
240

## Slide 242
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
6
STEP 6 OF 9
Enforce account lockout with pam_faillock
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
241

## Slide 243
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
7
STEP 7 OF 9
Enforce password aging
$ chage -M 90 -m 1 -W 7 alice
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
242

## Slide 244
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
8
STEP 8 OF 9
Layer file ACLs on top of group bits
$ setfacl -m g:netops:r-x /srv/dbdata
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
243

## Slide 245
LAB 20 · Identity & Access Management for S
Identity & Access Management for Server Administration
9
STEP 9 OF 9
Audit logins, group membership and account changes
$ getent group sysops dbops netops
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
244

## Slide 246
LAB 20 · VERIFY
Identity & Access Management for Server Administration
✅ Test it
The learner verifies success by confirming a user is denied a command outside its role and password/lockout policy is enforced.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
245

## Slide 247
TOPIC 03 · HANDS-ON
Multi-Factor Authentication with TOTP (PAM)
LAB 21
The learner adds a TOTP second factor to SSH with PAM, provisions a user's secret, generates codes from the CLI and tests the two-factor login.
You'll build
An SSH login enforcing a password plus a TOTP second factor.
Tools: libpam-google-authenticator, qrencode, oathtool
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
246

## Slide 248
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
1
STEP 1 OF 9
Install the MFA tools and start ssh
$ apt update && apt install -y libpam-google-authenticator qrencode oathtool openssh-server
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
247

## Slide 249
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
2
STEP 2 OF 9
Create a non-privileged user
$ useradd -m -s /bin/bash mfauser
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
248

## Slide 250
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
3
STEP 3 OF 9
Provision the TOTP secret for that user
$ sudo -u mfauser google-authenticator -t -d -f -r 3 -R 30 -w 17 -Q UTF8
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
249

## Slide 251
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
4
STEP 4 OF 9
Wire PAM and sshd to require TOTP
$ echo 'auth required pam_google_authenticator.so nullok' > /etc/pam.d/sshd.mfa
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
250

## Slide 252
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
5
STEP 5 OF 9
Enable challenge-response and restart ssh
$ systemctl restart ssh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
251

## Slide 253
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
6
STEP 6 OF 9
Generate the current TOTP from the CLI for testing
$ oathtool --totp -b "$SECRET"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
252

## Slide 254
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
7
STEP 7 OF 9
Test the two-factor login
$ ssh -o PreferredAuthentications=keyboard-interactive,password -o PubkeyAuthentication=no mfauser@127.0.0.1
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
253

## Slide 255
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
8
STEP 8 OF 9
Review scratch codes for account recovery
$ sudo tail -5 /home/mfauser/.google_authenticator
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
254

## Slide 256
LAB 21 · Multi-Factor Authentication with T
Multi-Factor Authentication with TOTP (PAM)
9
STEP 9 OF 9
Review the factor-category test for true MFA
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
255

## Slide 257
LAB 21 · VERIFY
Multi-Factor Authentication with TOTP (PAM)
✅ Test it
The learner verifies success by confirming login is denied with a wrong TOTP code even when the password is correct.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
256

## Slide 258
TOPIC 03 · HANDS-ON
Auditing, Logging, and SIEM Basics
LAB 22
The learner writes auditd rules for the four audit targets, configures rsyslog forwarding and rotation, runs logwatch and simulates a SIEM correlation rule.
You'll build
Auditd file-watch rules, log rotation policy and a simulated correlation alert.
Tools: auditd, rsyslog, logwatch
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
257

## Slide 259
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
1
STEP 1 OF 8
Install and enable auditd and rsyslog
$ apt update && apt install -y auditd audispd-plugins rsyslog logwatch
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
258

## Slide 260
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
2
STEP 2 OF 8
Write auditd rules for user/group/login/deletion events
$ augenrules --load
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
259

## Slide 261
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
3
STEP 3 OF 8
Trigger and search an audit event
$ ausearch -k id_changes -ts recent | tail -20
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
260

## Slide 262
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
4
STEP 4 OF 8
Review rsyslog severity levels and forwarding
$ logger -p auth.notice "Server+ lab test: notice-level entry"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
261

## Slide 263
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
5
STEP 5 OF 8
Configure log rotation and retention
$ logrotate -d /etc/logrotate.d/srvplus 2>&1 | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
262

## Slide 264
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
6
STEP 6 OF 8
Generate a daily report with logwatch
$ logwatch --output stdout --range today --detail Med | head -60
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
263

## Slide 265
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
7
STEP 7 OF 8
Simulate a SIEM correlation rule with awk
$ awk '/sshd.*Failed/ {fails[$NF]++} /sshd.*Accepted/ {if (fails[$NF]>=5) print "ALERT: brute then success from", $NF}' /var/log/auth.log
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
264

## Slide 266
LAB 22 · Auditing, Logging, and SIEM Basics
Auditing, Logging, and SIEM Basics
8
STEP 8 OF 8
Review two-person integrity and separation of roles
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
265

## Slide 267
LAB 22 · VERIFY
Auditing, Logging, and SIEM Basics
✅ Test it
The learner verifies success by finding the triggered auditd event and confirming the correlation rule and rotation config work.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
266

## Slide 268
TOPIC 03 · HANDS-ON
OS and Application Hardening
LAB 23
The learner baselines with Lynis, minimises services/ports/packages, hardens nginx, deploys AIDE and AppArmor, and re-scans to watch the hardening index climb.
You'll build
A hardened host with a rising Lynis index, AIDE baseline and AppArmor enforcement.
Tools: lynis, apparmor-utils, aide, chkrootkit
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
267

## Slide 269
LAB 23 · OS and Application Hardening
OS and Application Hardening
1
STEP 1 OF 9
Install the hardening tools
$ apt update && apt install -y lynis apparmor-utils debsums aide chkrootkit unattended-upgrades
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
268

## Slide 270
LAB 23 · OS and Application Hardening
OS and Application Hardening
2
STEP 2 OF 9
Baseline the host with Lynis and note the hardening index
$ lynis audit system --quick 2>&1 | tail -60
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
269

## Slide 271
LAB 23 · OS and Application Hardening
OS and Application Hardening
3
STEP 3 OF 9
Disable unused services
$ systemctl disable --now "$s"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
270

## Slide 272
LAB 23 · OS and Application Hardening
OS and Application Hardening
4
STEP 4 OF 9
Close unneeded ports with the firewall
$ ufw default deny incoming
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
271

## Slide 273
LAB 23 · OS and Application Hardening
OS and Application Hardening
5
STEP 5 OF 9
Remove unneeded packages (minimisation)
$ apt purge -y telnet ftp rsh-client 2>/dev/null
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
272

## Slide 274
LAB 23 · OS and Application Hardening
OS and Application Hardening
6
STEP 6 OF 9
Harden the nginx web role
$ nginx -t 2>/dev/null && systemctl reload nginx 2>/dev/null
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
273

## Slide 275
LAB 23 · OS and Application Hardening
OS and Application Hardening
7
STEP 7 OF 9
Build an AIDE file-integrity baseline and check
$ aideinit -y -f 2>&1 | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
274

## Slide 276
LAB 23 · OS and Application Hardening
OS and Application Hardening
8
STEP 8 OF 9
Enforce an AppArmor profile (MAC)
$ aa-enforce /etc/apparmor.d/usr.sbin.nginx 2>/dev/null
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
275

## Slide 277
LAB 23 · OS and Application Hardening
OS and Application Hardening
9
STEP 9 OF 9
Re-scan with Lynis and compare the score
$ lynis audit system --quick 2>&1 | grep -E "Hardening index|warning|suggestion" | tail -20
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
276

## Slide 278
LAB 23 · VERIFY
OS and Application Hardening
✅ Test it
The learner verifies success by confirming the Lynis hardening index improves after the minimisation and hardening steps.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
277

## Slide 279
TOPIC 03 · HANDS-ON
Patch and Update Management
LAB 24
The learner distinguishes security from feature updates, snapshots and smoke-tests, applies patches with change discipline, and configures security-only auto-apply with a rollback plan.
You'll build
A security-only unattended-upgrades config plus a patch report and rollback pin.
Tools: unattended-upgrades, needrestart, debsecan
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
278

## Slide 280
LAB 24 · Patch and Update Management
Patch and Update Management
1
STEP 1 OF 9
Install the patching tools
$ apt update && apt install -y unattended-upgrades needrestart apt-listchanges debsecan
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
279

## Slide 281
LAB 24 · Patch and Update Management
Patch and Update Management
2
STEP 2 OF 9
Inventory current package versions as a baseline
$ apt list --upgradable 2>/dev/null | head -20
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
280

## Slide 282
LAB 24 · Patch and Update Management
Patch and Update Management
3
STEP 3 OF 9
Identify security-only updates
$ apt-get -s dist-upgrade | grep -i security | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
281

## Slide 283
LAB 24 · Patch and Update Management
Patch and Update Management
4
STEP 4 OF 9
Apply patches with change-management discipline
$ DEBIAN_FRONTEND=noninteractive apt -y -o Dpkg::Options::="--force-confdef" -o Dpkg::Options::="--force-confold" upgrade
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
282

## Slide 284
LAB 24 · Patch and Update Management
Patch and Update Management
5
STEP 5 OF 9
Check which services need restarting after upgrade
$ needrestart -b
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
283

## Slide 285
LAB 24 · Patch and Update Management
Patch and Update Management
6
STEP 6 OF 9
Check whether a reboot is required
$ [ -f /var/run/reboot-required ] && cat /var/run/reboot-required
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
284

## Slide 286
LAB 24 · Patch and Update Management
Patch and Update Management
7
STEP 7 OF 9
Configure unattended-upgrades for security-only auto-apply
$ unattended-upgrade --dry-run -d 2>&1 | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
285

## Slide 287
LAB 24 · Patch and Update Management
Patch and Update Management
8
STEP 8 OF 9
Plan a rollback via package pinning
$ apt-mark hold nginx
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
286

## Slide 288
LAB 24 · Patch and Update Management
Patch and Update Management
9
STEP 9 OF 9
Write a patch report for the change ticket
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
287

## Slide 289
LAB 24 · VERIFY
Patch and Update Management
✅ Test it
The learner verifies success by confirming the security-only auto-apply config validates and a rollback pin holds the package version.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
288

## Slide 290
TOPIC 03 · HANDS-ON
Secure Decommissioning and Media Destruction
LAB 25
The learner works the decommission checklist, wipes a loopback image with shred and nwipe, and reviews SSD erase, physical destruction and recycling.
You'll build
A securely wiped media image with a documented decommission and destruction trail.
Tools: shred, wipe, nwipe, dd
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
289

## Slide 291
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
1
STEP 1 OF 9
Install the wipe tools
$ apt update && apt install -y wipe nwipe secure-delete
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
290

## Slide 292
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
2
STEP 2 OF 9
Review the decommission workflow checklist
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
291

## Slide 293
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
3
STEP 3 OF 9
Create a drive image with sensitive content
$ strings /srv/oldserver.img | grep -E "pii|cred" | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
292

## Slide 294
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
4
STEP 4 OF 9
Logically wipe with shred (single pass)
$ shred -v -n 1 -z /srv/oldserver.img
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
293

## Slide 295
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
5
STEP 5 OF 9
Confirm no plaintext is recoverable
$ strings /srv/oldserver.img | grep -E "pii|cred" | head || echo "no plaintext recoverable"
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
294

## Slide 296
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
6
STEP 6 OF 9
Multi-pass wipe with nwipe (DoD method)
$ nwipe --autonuke --nowait --method=dod /srv/oldserver.img 2>&1 | tail -10
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
295

## Slide 297
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
7
STEP 7 OF 9
Review SSD-specific ATA Secure Erase and crypto-erase
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
296

## Slide 298
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
8
STEP 8 OF 9
Review physical destruction methods (degauss, shred, crush, incinerate)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
297

## Slide 299
LAB 25 · Secure Decommissioning and Media D
Secure Decommissioning and Media Destruction
9
STEP 9 OF 9
Review cable remediation and internal vs external recycling
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
298

## Slide 300
LAB 25 · VERIFY
Secure Decommissioning and Media Destruction
✅ Test it
The learner verifies success by confirming the sensitive strings are unrecoverable after the wipe.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
299

## Slide 301
TOPIC 03 · HANDS-ON
Backup Strategy: Full, Incremental, Differential, Snapshot
LAB 26
The learner runs full, incremental and differential backups with tar, a deduplicated synthetic full with restic, and validates a restore against the source.
You'll build
A validated backup set spanning full, incremental, differential and restic snapshots.
Tools: tar, rsync, restic, lvm2
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
300

## Slide 302
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
1
STEP 1 OF 9
Install the backup tools
$ apt update && apt install -y rsync restic lvm2
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
301

## Slide 303
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
2
STEP 2 OF 9
Prepare a live dataset and backup target
$ for i in $(seq 1 10); do dd if=/dev/urandom of=/srv/data/file$i.bin bs=1K count=$((RANDOM%50+5)) 2>/dev/null; done
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
302

## Slide 304
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
3
STEP 3 OF 9
Take a full backup with tar
$ tar -czf /srv/backup/full-$(date +%F).tgz -C /srv data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
303

## Slide 305
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
4
STEP 4 OF 9
Take an incremental backup with a snapshot file
$ tar --listed-incremental=/srv/backup/snap.snar -czf /srv/backup/inc-$(date +%F).tgz -C /srv data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
304

## Slide 306
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
5
STEP 5 OF 9
Take a differential backup
$ tar --listed-incremental=/srv/backup/snap-full.snar -czf /srv/backup/diff-$(date +%F).tgz -C /srv data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
305

## Slide 307
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
6
STEP 6 OF 9
Take deduplicated synthetic-full snapshots with restic
$ restic -r /srv/backup/restic backup /srv/data
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
306

## Slide 308
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
7
STEP 7 OF 9
Review media types and GFS rotation
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
307

## Slide 309
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
8
STEP 8 OF 9
Restore side-by-side and to an alternate location
$ restic -r /srv/backup/restic restore latest --target /srv/restore-alt
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
308

## Slide 310
LAB 26 · Backup Strategy: Full, Incremental
Backup Strategy: Full, Incremental, Differential, Snapshot
9
STEP 9 OF 9
Validate integrity and diff the restore against source
$ restic -r /srv/backup/restic check
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
309

## Slide 311
LAB 26 · VERIFY
Backup Strategy: Full, Incremental, Differential, Snapshot
✅ Test it
The learner verifies success by confirming the restic integrity check passes and the restored data matches the source.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
310

## Slide 312
TOPIC 03 · HANDS-ON
Disaster Recovery: Replication and Site Failover
LAB 27
The learner replicates data async with rsync and near-sync with lsyncd, reviews sync/DRBD concepts, plans keepalived VIP failover and runs a tabletop DR exercise.
You'll build
An async and near-real-time replication pair plus a DR tabletop exercise plan.
Tools: rsync, lsyncd, keepalived, inotify-tools
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
311

## Slide 313
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
1
STEP 1 OF 9
Install the DR tools
$ apt update && apt install -y rsync lsyncd keepalived inotify-tools
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
312

## Slide 314
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
2
STEP 2 OF 9
Review hot/warm/cold/cloud site types
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
313

## Slide 315
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
3
STEP 3 OF 9
Replicate asynchronously with rsync
$ rsync -avh --delete /srv/primary/ /srv/dr/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
314

## Slide 316
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
4
STEP 4 OF 9
Configure near-real-time replication with lsyncd
$ systemctl restart lsyncd
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
315

## Slide 317
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
5
STEP 5 OF 9
Confirm the change propagated to the DR copy
$ cat /srv/dr/app.txt
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
316

## Slide 318
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
6
STEP 6 OF 9
Review synchronous replication (DRBD, semi-sync DB) trade-offs
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
317

## Slide 319
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
7
STEP 7 OF 9
Plan a keepalived VIP failover for DR cut-over
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
318

## Slide 320
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
8
STEP 8 OF 9
Review the four DR test types
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
319

## Slide 321
LAB 27 · Disaster Recovery: Replication and
Disaster Recovery: Replication and Site Failover
9
STEP 9 OF 9
Run the tabletop DR exercise and capture action items
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
320

## Slide 322
LAB 27 · VERIFY
Disaster Recovery: Replication and Site Failover
✅ Test it
The learner verifies success by confirming a change on the primary appears in the DR copy within seconds via lsyncd.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
321

## Slide 323
TOPIC RECAP
Recap — Security and Disaster Recovery
• You can now: 3.1 Data security concepts (encryption at rest and in transit)
• You can now: 3.2 Physical security concepts
• You can now: 3.3 Identity and access management
• You can now: 3.3 Multifactor authentication
• You can now: 3.4 Data security risks and mitigation (log analysis, SIEM)
• You can now: 3.5 Apply server hardening methods
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
322

## Slide 324
TOPIC 04
Troubleshooting
Structured methodology · hardware · storage · OS/software · network · DR validation
04
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
323

## Slide 325
EXAM WEIGHTING 28%
Key Concepts — Troubleshooting
1
Methodology
The CompTIA 6-step model: identify the problem, theorise, test, plan, implement & verify, document — change one thing at a time.
2
Hardware faults
Power issues, POST/beep codes, failed drives (smartctl), overheating and memory errors (memtester, sensors).
3
Storage faults
Degraded/failed arrays, full or corrupt file systems (fsck), I/O bottlenecks and open-file locks.
4
OS & software faults
Boot and service failures (systemd, journalctl), failed patches, dependency and permission errors.
5
Network faults
Latency, DNS and gateway misconfiguration, packet loss and cabling — diagnosed with ping, mtr, dig and tcpdump.
6
DR validation
Testing backups and restores, verifying failover, and confirming RPO/RTO are actually met.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
324

## Slide 326
WHAT YOU'LL DO
Hands-On Labs — Troubleshooting
Labs 28–29
• Troubleshooting Methodology Walk-Through
• Troubleshooting Common Hardware Failures
Labs 30–31
• Storage Troubleshooting
• OS and Software Troubleshooting
Labs 32–33
• Network Connectivity Troubleshooting
• Security Troubleshooting
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
325

## Slide 327
TOPIC 04 · HANDS-ON
Troubleshooting Methodology Walk-Through
LAB 28
The learner breaks nginx, then applies the Server+ 7-step methodology end-to-end from identifying the problem through root-cause analysis and documentation.
You'll build
A resolved incident with an RCA and a documented post-incident record.
Tools: nginx, journalctl, ss, systemctl
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
326

## Slide 328
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
1
STEP 1 OF 9
Manufacture a fault by breaking the nginx listen port
$ sed -i 's/listen 80;/listen 22;/' /etc/nginx/sites-enabled/default
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
327

## Slide 329
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
2
STEP 2 OF 9
Identify the problem and scope by collecting logs
$ journalctl -u nginx -n 40 --no-pager
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
328

## Slide 330
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
3
STEP 3 OF 9
Replicate the fault from the server itself
$ curl -sI http://127.0.0.1/ 2>&1 | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
329

## Slide 331
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
4
STEP 4 OF 9
Back up the config before making changes
$ cp /etc/nginx/sites-enabled/default /root/default.pre-fix.$(date +%s)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
330

## Slide 332
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
5
STEP 5 OF 9
Establish and test a theory (port 22 already in use)
$ ss -tlnp 'sport = :22'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
331

## Slide 333
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
6
STEP 6 OF 9
Implement the solution, one change at a time
$ sed -i 's/listen 22;/listen 80;/' /etc/nginx/sites-enabled/default
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
332

## Slide 334
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
7
STEP 7 OF 9
Verify full system functionality including dependencies
$ curl -sI http://127.0.0.1/ | head -1
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
333

## Slide 335
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
8
STEP 8 OF 9
Add a preventive config-validation measure
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
334

## Slide 336
LAB 28 · Troubleshooting Methodology Walk-T
Troubleshooting Methodology Walk-Through
9
STEP 9 OF 9
Perform a 5-whys root-cause analysis and document it
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
335

## Slide 337
LAB 28 · VERIFY
Troubleshooting Methodology Walk-Through
✅ Test it
The learner verifies success by confirming nginx returns HTTP 200 and produces a documented RCA record.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
336

## Slide 338
TOPIC 04 · HANDS-ON
Troubleshooting Common Hardware Failures
LAB 29
The learner reads event logs first, stress-tests CPU thermals, checks memory/ECC and SMART predictive failures, and maps POST/LED/olfactory cues to causes.
You'll build
A hardware fault decision tree exercised against event logs, sensors and SMART.
Tools: dmesg, smartmontools, lm-sensors, memtester
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
337

## Slide 339
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
1
STEP 1 OF 9
Install the hardware diagnostic tools
$ apt update && apt install -y dmidecode lshw smartmontools lm-sensors memtester stress-ng edac-utils
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
338

## Slide 340
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
2
STEP 2 OF 9
Check event logs first for hardware faults
$ journalctl -k | grep -iE 'mce|edac|temperature|throttl|over.?heat|ecc' | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
339

## Slide 341
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
3
STEP 3 OF 9
Stress-test CPU and read thermals/utilisation
$ stress-ng --cpu $(nproc) --timeout 10s --metrics-brief 2>&1 | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
340

## Slide 342
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
4
STEP 4 OF 9
Check memory errors, ECC and crash-dump terms
$ dmesg | grep -i mce | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
341

## Slide 343
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
5
STEP 5 OF 9
Read SMART predictive-failure attributes
$ smartctl -a /dev/sda 2>/dev/null | head -40
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
342

## Slide 344
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
6
STEP 6 OF 9
Review PSU/fan faults via the BMC SEL
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
343

## Slide 345
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
7
STEP 7 OF 9
Review CMOS battery failure symptoms
$ chronyc tracking 2>/dev/null | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
344

## Slide 346
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
8
STEP 8 OF 9
Map POST codes and visual/auditory/olfactory cues to causes
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
345

## Slide 347
LAB 29 · Troubleshooting Common Hardware Fa
Troubleshooting Common Hardware Failures
9
STEP 9 OF 9
Distinguish host-hardware faults from misallocated-VM symptoms
$ iostat -x 1 3
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
346

## Slide 348
LAB 29 · VERIFY
Troubleshooting Common Hardware Failures
✅ Test it
The learner verifies success by mapping each Server+ 4.2 symptom to a concrete tool and reading SMART health for predictive failure.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
347

## Slide 349
TOPIC 04 · HANDS-ON
Storage Troubleshooting
LAB 30
The learner diagnoses disk/inode-full and slow I/O, recovers a corrupt superblock, rebuilds a failed RAID drive, and reviews cache-battery and cable faults.
You'll build
Recovered filesystems and a rebuilt RAID array with a storage-fault tool map.
Tools: mdadm, e2fsprogs, lsof, iotop
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
348

## Slide 350
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
1
STEP 1 OF 9
Install the storage diagnostic tools
$ apt update && apt install -y mdadm lvm2 e2fsprogs xfsprogs parted gdisk smartmontools lsof iotop sysstat
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
349

## Slide 351
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
2
STEP 2 OF 9
Check capacity and inode utilisation
$ df -i
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
350

## Slide 352
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
3
STEP 3 OF 9
Diagnose slow I/O with iostat and iotop
$ iostat -xz 1 5
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
351

## Slide 353
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
4
STEP 4 OF 9
Corrupt and then recover a filesystem via a backup superblock
$ fsck.ext4 -b 32768 $LOOP || true
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
352

## Slide 354
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
5
STEP 5 OF 9
Create a RAID 5 array and fail a drive
$ mdadm /dev/md30 --fail /dev/loop32 --remove /dev/loop32
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
353

## Slide 355
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
6
STEP 6 OF 9
Add a spare and watch the array rebuild
$ mdadm /dev/md30 --add /dev/loop35
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
354

## Slide 356
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
7
STEP 7 OF 9
Review cache-battery failure and write slowdown
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
355

## Slide 357
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
8
STEP 8 OF 9
Read OS clues for cable/connector/backplane faults
$ dmesg | grep -iE "ata|scsi|sas|link rate|hard reset" | tail
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
356

## Slide 358
LAB 30 · Storage Troubleshooting
Storage Troubleshooting
9
STEP 9 OF 9
Diagnose page/swap errors
$ swapon --show
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
357

## Slide 359
LAB 30 · VERIFY
Storage Troubleshooting
✅ Test it
The learner verifies success by mounting the recovered filesystem and confirming the RAID array rebuilds in /proc/mdstat.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
358

## Slide 360
TOPIC 04 · HANDS-ON
OS and Software Troubleshooting
LAB 31
The learner triages systemd services, fixes clock skew and broken dpkg state, reviews recovery boot modes, and uses Ansible to prevent config drift.
You'll build
A recovered service and package state plus an idempotent Ansible playbook.
Tools: systemd, strace, chrony, ansible
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
359

## Slide 361
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
1
STEP 1 OF 9
Install the OS troubleshooting tools
$ apt update && apt install -y strace chrony ansible
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
360

## Slide 362
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
2
STEP 2 OF 9
Triage a service: status, dependencies, failed units
$ systemctl list-units --type=service --state=failed
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
361

## Slide 363
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
3
STEP 3 OF 9
Diagnose a hanging service with strace
$ strace -p $PID -e trace=accept4,read,write -c -f -t -o /tmp/strace.log &
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
362

## Slide 364
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
4
STEP 4 OF 9
Diagnose and fix clock skew that breaks auth
$ chronyc -a 'burst 4/4'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
363

## Slide 365
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
5
STEP 5 OF 9
Recover from a broken dpkg/patch state
$ dpkg --configure -a 2>&1 | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
364

## Slide 366
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
6
STEP 6 OF 9
Check missing dependencies and downstream failures
$ apt-cache rdepends openssl | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
365

## Slide 367
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
7
STEP 7 OF 9
Review recovery boot modes (rescue, emergency, snapshot)
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
366

## Slide 368
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
8
STEP 8 OF 9
Diagnose memory leak and set CPU affinity/priority
$ ps -eo pid,comm,rss,nice,psr --sort=-rss | head -10
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
367

## Slide 369
LAB 31 · OS and Software Troubleshooting
OS and Software Troubleshooting
9
STEP 9 OF 9
Prevent config drift with an idempotent Ansible playbook
$ ansible-playbook playbook.yml 2>&1 | tail -10
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
368

## Slide 370
LAB 31 · VERIFY
OS and Software Troubleshooting
✅ Test it
The learner verifies success by confirming the service and package state recover and the Ansible playbook reports no changes on a second run.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
369

## Slide 371
TOPIC 04 · HANDS-ON
Network Connectivity Troubleshooting
LAB 32
The learner triages 'I can't reach the server' bottom-up through the OSI layers using ip, ping, traceroute, dig, nc and tcpdump.
You'll build
A repeatable bottom-up network triage exercised layer by layer.
Tools: iproute2, dnsutils, tcpdump, mtr-tiny
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
370

## Slide 372
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
1
STEP 1 OF 9
Install the network diagnostic tools
$ apt update && apt install -y iproute2 iputils-ping dnsutils tcpdump mtr-tiny traceroute nmap netcat-openbsd
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
371

## Slide 373
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
2
STEP 2 OF 9
Layer 1: check link, cable and NIC state
$ ethtool eth0 2>/dev/null | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
372

## Slide 374
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
3
STEP 3 OF 9
Layer 2: check NIC config and the ARP table
$ ip neigh
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
373

## Slide 375
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
4
STEP 4 OF 9
Layer 3: check addressing, gateway and routes
$ ip route get 8.8.8.8
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
374

## Slide 376
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
5
STEP 5 OF 9
Test reachability with ping, traceroute and mtr
$ mtr -rwc 5 8.8.8.8 2>/dev/null | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
375

## Slide 377
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
6
STEP 6 OF 9
Resolve names down the DNS chain
$ dig +short example.com
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
376

## Slide 378
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
7
STEP 7 OF 9
Test port reachability with nc and nmap
$ nc -vz example.com 80 2>&1 | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
377

## Slide 379
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
8
STEP 8 OF 9
Capture packets to find the silent direction
$ tcpdump -ni eth0 -c 10 'icmp or port 53' 2>&1 | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
378

## Slide 380
LAB 32 · Network Connectivity Troubleshooti
Network Connectivity Troubleshooting
9
STEP 9 OF 9
Work the bottom-up decision tree
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
379

## Slide 381
LAB 32 · VERIFY
Network Connectivity Troubleshooting
✅ Test it
The learner verifies success by walking a connectivity failure layer by layer and pinpointing the drop with tcpdump.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
380

## Slide 382
TOPIC 04 · HANDS-ON
Security Troubleshooting
LAB 33
The learner audits open ports and process states, checks file integrity with AIDE, hunts privilege-escalation misconfigs and runs an anti-malware scan.
You'll build
A security triage covering ports, processes, file integrity and malware.
Tools: nmap, lsof, aide, chkrootkit, clamav
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
381

## Slide 383
LAB 33 · Security Troubleshooting
Security Troubleshooting
1
STEP 1 OF 9
Install the security troubleshooting tools
$ apt update && apt install -y nmap lsof aide chkrootkit clamav clamav-daemon auditd
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
382

## Slide 384
LAB 33 · Security Troubleshooting
Security Troubleshooting
2
STEP 2 OF 9
Audit open ports against the firewall policy
$ nmap -sT -p- -T4 127.0.0.1 2>/dev/null | head -30
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
383

## Slide 385
LAB 33 · Security Troubleshooting
Security Troubleshooting
3
STEP 3 OF 9
Classify process states: active, orphan, zombie
$ ps -eo pid,ppid,state,user,comm | awk '$3=="Z"'
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
384

## Slide 386
LAB 33 · Security Troubleshooting
Security Troubleshooting
4
STEP 4 OF 9
Scan for rogue processes and rootkits
$ chkrootkit | head -30
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
385

## Slide 387
LAB 33 · Security Troubleshooting
Security Troubleshooting
5
STEP 5 OF 9
Baseline and check file integrity with AIDE
$ aide --check 2>&1 | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
386

## Slide 388
LAB 33 · Security Troubleshooting
Security Troubleshooting
6
STEP 6 OF 9
Hunt world-writable, SUID and writable-sudoers misconfigs
$ find / -xdev \( -perm -4000 -o -perm -2000 \) -type f 2>/dev/null | head
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
387

## Slide 389
LAB 33 · Security Troubleshooting
Security Troubleshooting
7
STEP 7 OF 9
Run an anti-malware scan with the EICAR test file
$ clamscan /tmp/scan/ 2>&1 | tail -10
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
388

## Slide 390
LAB 33 · Security Troubleshooting
Security Troubleshooting
8
STEP 8 OF 9
Triage 'cannot open file': perms, MAC policy, service health
$ getfacl /srv/share/
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
389

## Slide 391
LAB 33 · Security Troubleshooting
Security Troubleshooting
9
STEP 9 OF 9
Work the security decision tree
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
390

## Slide 392
LAB 33 · VERIFY
Security Troubleshooting
✅ Test it
The learner verifies success by detecting the AIDE integrity drift and the EICAR test file with ClamAV.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
391

## Slide 393
TOPIC RECAP
Recap — Troubleshooting
• You can now: 4.1 Troubleshooting theory and methodology
• You can now: 4.2 Troubleshoot common hardware failures
• You can now: 4.3 Troubleshoot storage problems
• You can now: 4.4 Troubleshoot common OS and software problems
• You can now: 4.5 Troubleshoot network connectivity issues
• You can now: 4.6 Troubleshoot security problems
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
392

## Slide 394
WRAP-UP
Course Summary & Next Steps
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
393

## Slide 395
LEARNING OUTCOMES
What You Achieved
1
Hardware & Storage
Racked and powered servers; built RAID 0/1/5/6/10 and LVM; deployed NFS/iSCSI; managed firmware and out-of-band.
2
Server Administration
Installed operating systems and file systems; configured IP/DNS/DHCP; ran web/file/DB/LDAP roles, HA, KVM and scripts.
3
Security & DR
Encrypted data at rest and in transit; managed IAM and MFA; hardened and audited hosts; wiped media; built backups and DR.
4
Troubleshooting
Diagnosed hardware, storage, OS, software and network faults with the CompTIA 6-step methodology.
5
Exam readiness
Mapped every lab to an SK0-005 exam objective across all four domains.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
394

## Slide 396
NEXT STEPS
Preparing for the SK0-005 Exam
• Redo every lab from memory until the command workflow and flags are automatic.
• Review the 'What you learned' bullets in each lab and the Learner Guide.
• Practise the RAID capacity/fault-tolerance formulas, subnetting, and the 6-step troubleshooting model.
• Take the free CompTIA practice assessment for Server+ SK0-005.
• Book the exam via a Pearson VUE test centre or online proctoring.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
395

## Slide 397
TEST YOURSELF
Practice Exam
• Sharpen your exam readiness with the Tertiary Infotech CompTIA Server+ practice exam.
• Practice exam: https://exams.tertiaryinfotech.com/practice-exams/comptia/comptia-server-plus
• Attempt it under timed conditions and review every explanation.
• Revisit any lab whose topic you miss, then re-take the practice exam.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
396

## Slide 398
WRAP-UP
Assessment
• Written Assessment (SAQ) — 1 hour. Practical Performance (PP) — 1 hour.
• Open book: slides, Learner Guide and approved materials only.
• Remember to take the Assessment digital attendance (TRAQOM).
• Submit your completed answers on the LMS at https://lms-tms.tertiaryinfotech.com/.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
397

## Slide 399
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit WA (SAQ) then PP — open book
▶
4
Submit your answers on the LMS
▶
5
Sign the Assessment Summary Record
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
398

## Slide 400
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
• It is mandatory to take the AM, PM and Assessment digital attendance for WSQ-funded courses.
• The trainer/administrator displays the digital attendance QR code from the SSG portal.
• Scan the QR code with your mobile phone camera and submit your attendance.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
399

## Slide 401
YOU'RE SERVER+ READY
Thank You!
You are now ready to install, administer, secure and troubleshoot servers — and to sit the CompTIA Server+ (SK0-005) exam.
CompTIA Certified Server Plus Training · TGS-2024048318
© 2026 Tertiary Infotech Academy Pte Ltd
400